By:  Greenberg	H.B. No. 283

A BILL TO BE ENTITLED

AN ACT

relating to barriers around residential swimming pools.

BE IT ENACTED BY THE LEGISLATURE OF THE STATE OF TEXAS:

SECTION 1.  Subtitle A, Title 9, Health and Safety Code, is amended by adding Chapter 757 to read as follows:

CHAPTER 757.  BARRIERS AROUND RESIDENTIAL SWIMMING POOLS

Sec. 757.001.  DEFINITIONS.  In this chapter:

(1)  "Barrier" means a fence, dwelling wall, nondwelling wall, or a combination of fences and walls that completely surrounds a swimming pool and obstructs access to the swimming pool.

(2)  "Indoor swimming pool" means a swimming pool that is totally contained within a building and surrounded on all four sides by the walls of the building.

(3)  "Outdoor swimming pool" means a swimming pool that is not an indoor swimming pool.

(4)  "Portable spa" means a nonpermanent structure intended for recreational bathing in which all controls, water-heating, and water-circulating equipment are an integral part of the product and that is cord-connected and not permanently electrically wired.

(5)  "Residential" means that which is located on the premises of a detached one- or two-family dwelling or a one-family townhouse not more than three stories high.

(6)  "Swimming pool" means a structure that is intended for swimming or recreational bathing and that contains water over 24 inches deep, including an inground, aboveground, or onground swimming pool, a hot tub, and a spa.

Sec. 757.002.  APPLICATION; EXEMPTION. (a)  This chapter applies only to a swimming pool that is located on the premises of a detached one- or two-family dwelling or of a one-family townhouse not more than three stories high.

(b)  This chapter does not apply to a portable spa if it has a safety cover that complies with the American Society of Testing Materials Standard ASTM F1346-91.

Sec. 757.003.  BARRIER AROUND OUTDOOR SWIMMING POOL. An outdoor residential swimming pool shall have a barrier that complies with Sections 757.004-757.008.

Sec. 757.004.  HEIGHT AND LOCATION OF BARRIER. (a)  The top of a barrier for an outdoor residential swimming pool shall be at least 48 inches above the grade as measured on the side of the barrier that faces away from the swimming pool.

(b)  The vertical clearance between the grade and the bottom of the barrier may not exceed four inches as measured on the side of the barrier that faces away from the swimming pool.

(c)  If the top of a pool structure is above the grade, such as an aboveground pool, the barrier may be at ground level or mounted on top of the pool structure.

(d)  If a barrier is mounted on top of a pool structure, the vertical clearance between the top of the pool structure and the bottom of the barrier may not exceed four inches.

Sec. 757.005.  OPENINGS, INDENTATIONS, OR PROTRUSIONS IN BARRIER. (a)  An opening in a barrier for an outdoor residential swimming pool may not be of a size that would allow the passage of a sphere that is four inches in diameter.

(b)  A solid barrier that does not have an opening, including a masonry or stone wall, may not contain indentations or protrusions other than normal construction tolerances and tooled masonry joints.

Sec. 757.006.  BARRIER COMPOSED OF HORIZONTAL AND VERTICAL MEMBERS. (a)  If a barrier for an outdoor residential swimming pool is composed of horizontal and vertical members and the distance between the tops of the horizontal members is less than 45 inches:

(1)  the horizontal members shall be located on the side of the fence facing the swimming pool;

(2)  spacing between the vertical members may not exceed 1-3/4 inches in width; and

(3)  spacing within decorative cutouts may not exceed 1-3/4 inches in width.

(b)  If a barrier is composed of horizontal and vertical members and the distance between the tops of the horizontal members is 45 inches or more:

(1)  spacing between vertical members may not exceed four inches; and

(2)  spacing within decorative cutouts may not exceed 1-3/4 inches in width.

Sec. 757.007.  CHAIN LINK FENCE. The mesh size for a chain link fence that forms a barrier for an outdoor residential swimming pool may not exceed 1-1/4 inch square unless the fence has slats fastened at the top or bottom of the fence that reduce the openings to not more than 1-3/4 inches.

Sec. 757.008.  BARRIER COMPOSED OF DIAGONAL MEMBERS. If a barrier for an outdoor residential swimming pool is composed of diagonal members, such as a lattice fence, the opening formed by the diagonal members may not exceed 1-3/4 inches.

Sec. 757.009.  GATE THAT PROVIDES ACCESS TO OUTDOOR SWIMMING POOL. (a)  A gate that provides access to an outdoor residential swimming pool shall comply with Sections 757.004-757.008 and shall be equipped to accommodate a locking device.

(b)  A gate shall have a self-latching device.  In addition, a pedestrian access gate shall open outwards away from the swimming pool and shall be self-closing.

(c)  If the release mechanism of a self-latching device is located less than 54 inches from the bottom of the gate:

(1)  the release mechanism shall be located on the side of the gate facing the swimming pool and at least three inches below the top of the gate; and

(2)  the gate and barrier may not have an opening greater than one-half inch within 18 inches of the release mechanism.

Sec. 757.010.  WALL THAT FORMS PART OF BARRIER. (a)  This section applies to:

(1)  a wall of a dwelling that serves as part of a barrier for an outdoor residential swimming pool; and

(2)  each wall surrounding an indoor residential swimming pool.

(b)  A door that gives direct access to a swimming pool through the wall shall be equipped with an alarm that:

(1)  produces an audible warning when the door and its screen, if present, are opened;

(2)  sounds continuously for at least 30 seconds immediately after the door is opened;

(3)  has a minimum sound pressure rating of 85 dBa at 10 feet;

(4)  has a sound that is distinctive from other household sounds such as smoke alarms, telephones, and doorbells;

(5)  automatically resets under all conditions; and

(6)  is equipped with manual means, including touchpads or switches, to temporarily deactivate the alarm for a single opening from either direction.

(c)  The alarm deactivator required under Subsection (b)(6) may not allow the deactivation to last for more than 15 seconds.  The deactivation touchpads or switches shall be located at least 54 inches above the threshold of the door.

(d)  Subsections (b) and (c) do not apply if:

(1)  the swimming pool has a power safety cover that complies with the American Society of Testing Materials Standard ASTM F1346-91; or

(2)  there are other means of protecting the swimming pool that are at least as protective as the requirements of Subsections (b) and (c) and that are authorized by rule adopted by the Board of Public Health, such as self-closing mechanisms and self-latching devices on a door that has direct access to a swimming pool.

(e)  The Board of Public Health shall adopt rules to implement Subsection (d)(2).

Sec. 757.011.  ABOVEGROUND POOL LADDERS OR STEPS. (a)  If an aboveground pool structure is used as a barrier or the barrier is mounted on top of the pool structure and the means of access is a ladder or steps, the ladder or steps shall be:

(1)  capable of being secured, locked, or removed to prevent access; or

(2)  surrounded by a barrier that meets the requirements of Sections 757.004-757.010.

(b)  If the ladder or steps are secured, locked, or removed, any opening created may not be of a size that would allow the passage of a sphere that is four inches in diameter.

Sec. 757.012.  STRUCTURES USED FOR CLIMBING BARRIERS. A barrier for a residential swimming pool may not be located in a way that allows the use of a permanent structure, equipment, or other similar object to climb the barrier.

SECTION 2.  The Board of Public Health shall adopt rules under Sections 757.010(d)(2) and (e), Health and Safety Code, as added by this Act, not later than December 1, 1993.  Until those rules are adopted, a person desiring to use other means of protecting a swimming pool as authorized by that subdivision shall apply to the Board of Public Health for approval of the alternate means of protection.

SECTION 3.  This Act takes effect September 1, 1993, and applies only to a residential swimming pool for which initial construction begins on or after that date.

SECTION 4.  The importance of this legislation and the crowded condition of the calendars in both houses create an emergency   and   an   imperative   public   necessity   that   the constitutional rule requiring bills to be read on three several days in each house be suspended, and this rule is hereby suspended.