By Combs	H.B. No. 2137

A BILL TO BE ENTITLED

AN ACT

relating to pool and spa enclosures.

BE IT ENACTED BY THE LEGISLATURE OF THE STATE OF TEXAS:

SECTION 1.  Section 757.001, Health and Safety Code, is amended by amending Subdivisions (7), (8), and (10) to read as follows:

(7)  "Multiunit rental complex" means two or more dwelling units in one or more buildings that are under common ownership, managed by the same owner, managing agent, or management company, and located on the same lot or tract of land or adjacent lots or tracts of land.  [The term includes a condominium project.]  The term does not include:

(A)  a facility primarily renting rooms to overnight guests; [or]

(B)  a single-family home or adjacent single-family homes;

(C)  a duplex;

(D)  a triplex or quadraplex in which the owner is a resident; or

(E)  a condominium, cooperative, or town home project [that are not part of a condominium project].

(8)  "Pool" means a permanent swimming pool, permanent wading or reflection pool, or permanent hot tub or spa over 24 [18] inches deep, located at ground level, above ground, below ground, or indoors.

(10)  "Pool yard enclosure" or "enclosure" means a fence, wall, natural barrier, or combination of fences, walls, natural barriers, gates, windows, or doors that [completely] surround a pool.

SECTION 2.  Section 757.002, Health and Safety Code, is amended to read as follows:

Sec. 757.002.  APPLICATION.  This chapter applies only to:

(1)  a pool owned, controlled, or maintained by the state, by a municipality, by a business offering the use of a pool to the public for a fee, or by the owner of a multiunit rental complex [or by a property owners association]; and

(2)  doors and windows of rental dwellings opening into the pool yard of a multiunit rental complex [or condominium, cooperative, or town home project].

SECTION 3.  Section 757.003, Health and Safety Code, is amended to read as follows:

Sec. 757.003.  ENCLOSURE FOR POOL YARD.  (a)  Except as otherwise provided by Section 757.005, the owner of a pool covered by Section 757.002 [multiunit rental complex with a pool or a property owners association that owns, controls, or maintains a pool] shall [completely] enclose the pool yard with a pool yard enclosure so that the pool is not an attractive nuisance to children two years of age or younger.

(b)  The height of the pool yard enclosure must be at least 36 [48] inches as measured from the [ground on the] side of [away from] the pool appropriate to achieve the purpose provided by Subsection (a).

(c)  Openings under the pool yard enclosure may not allow a sphere five [four] inches in diameter to pass under the pool yard enclosure.

(d)  If the pool yard enclosure is constructed with horizontal and vertical members [and the distance between the tops of the horizontal members is at least 45 inches], the openings may not allow a sphere five [four] inches in diameter to pass through the enclosure.

(e)  [If the pool yard enclosure is constructed with horizontal and vertical members and the distance between the tops of the horizontal members is less than 45 inches, the openings may not allow a sphere 1 3/4  inches in diameter to pass through the enclosure.

[(f)  The use of chain link fencing materials is prohibited entirely for a new pool yard enclosure that is constructed after January 1, 1994.  The use of diagonal fencing members that are lower than 49 inches above the ground is prohibited for a new pool yard enclosure that is constructed after January 1, 1994.

[(g)  Decorative designs or cutouts on or in the pool yard enclosure may not contain any openings greater than 1 3/4 inches in any direction.

[(h)  Indentations or protrusions in a solid pool yard enclosure without any openings may not be greater than normal construction tolerances and tooled masonry joints on the side away from the pool.

[(i)  Permanent equipment or structures may not be constructed or placed in a manner that makes them readily available for climbing over the pool yard enclosure.

[(j)]  The wall of a building may be part of the pool yard enclosure [only] if the doors and windows in the wall comply with Sections 757.006 and 757.007.

(f) [(k)]  The owner of a [multiunit rental complex with a pool or a property owners association that owns, controls, or maintains a] pool is not required to:

(1)  build a pool yard enclosure at specified locations or distances from the pool other than distances for minimum walkways around the pool; or

(2)  conform secondary pool yard enclosures, located inside or outside the primary pool yard enclosure, to the requirements of this chapter.

SECTION 4.  Section 757.004, Health and Safety Code, is amended to read as follows:

Sec. 757.004.  GATES.  (a)  Except as otherwise provided by Section 757.005, a gate in a fence or wall enclosing a pool yard as required by Section 757.003 must:

(1)  have a self-closing and self-latching device; and

(2)  [have hardware enabling it to be locked, at the option of whoever controls the gate, by a padlock or a built-in lock operated by key, card, or combination; and

[(3)]  open outward away from the pool yard.

(b)  Except as otherwise provided by Subsection (c) and Section 757.005, a gate latch must be installed so that it is at least approximately 36 [60] inches above the ground, except that it may be installed lower if:

(1)  the latch is installed on the pool yard side of the gate only and is at least three inches below the top of the gate; and

(2)  the gate or enclosure has no opening greater than one-half inch in any direction within 18 inches from the latch, including the space between the gate and the gate post to which the gate latches.

(c)  A gate latch may be located anywhere on the gate [42 inches or higher above the ground] if the gate cannot be opened except by key, card, or combination [on both sides of the gate].

SECTION 5.  Section 757.005, Health and Safety Code, is amended to read as follows:

Sec. 757.005.  EXISTING POOL YARD ENCLOSURES.  [(a)  If a pool yard enclosure is constructed or modified before January 1, 1994, and no municipal ordinance containing standards for pool yard enclosures were applicable at the time of construction or modification, the enclosure must comply with the requirements of Sections 757.003 and 757.004, except that:

[(1)  if the enclosure is constructed with chain link metal fencing material, the openings in the enclosure may not allow a sphere 2 1/4 inches in diameter to pass through the enclosure; or

[(2)  if the enclosure is constructed with horizontal and vertical members and the distance between the tops of the horizontal members is at least 36 inches, the openings in the enclosure may not allow a sphere four inches in diameter to pass through the enclosure.

[(b)]  If a pool yard enclosure is constructed or modified before January 1, 1994, [and if the enclosure is in compliance with applicable municipal ordinances existing on January 1, 1994, and containing standards for pool yard enclosures,] Sections 757.003, 757.004(a)(2) [757.004(a)(3)], and 757.004(b) do not apply to the enclosure.

SECTION 6.  Section 757.006, Health and Safety Code, is amended to read as follows:

Sec. 757.006.  DOOR.  (a)  [A door, sliding glass door, or French door may not open directly into a pool yard if the date of electrical service for initial construction of the building or pool is on or after January 1, 1994.

[(b)  A door, sliding glass door, or French door may open directly into a pool yard if the date of electrical service for initial construction of the building or pool is before January 1, 1994, and the pool yard enclosure complies with Subsection (c), (d), or (e), as applicable.

[(c)]  If a door of a building, other than a sliding glass door or screen door, opens into the pool yard, the door must have a:

(1)  latch that automatically engages when the door is closed;

(2)  spring-loaded door-hinge pin, automatic door closer, or similar device to cause the door to close automatically; and

(3)  keyless bolting device that is installed not less than 36 inches [or more than 48 inches] above the interior floor.

(b) [(d)]  If French doors of a building open to the pool yard, one of the French doors must comply with Subsection (a)(1) [(c)(1)] and the other door must have:

(1)  a keyed dead bolt or keyless bolting device capable of insertion into the doorjamb above the door, and a keyless bolting device capable of insertion into the floor or threshold; or

(2)  a bolt with at least a 3/4-inch throw installed inside the door and operated from the edge of the door that is capable of insertion into the doorjamb above the door and another bolt with at least a 3/4-inch throw installed inside the door and operated from the edge of the door that is capable of insertion into the floor or threshold.

(c) [(e)]  If a sliding glass door of a building opens into the pool yard, the sliding glass door must have:

(1)  a sliding door handle latch or sliding door security bar that is installed not more than 48 inches above the interior floor; or [and]

(2)  a sliding door pin lock that is installed not more than 48 inches above the interior floor.

(d) [(f)]  A door, sliding glass door, or French door that opens into a pool yard from an area of a building that is not used by residents and that has no access to an area outside the pool yard is not required to have a lock, latch, dead bolt, or keyless bolting device.

(e) [(g)]  A keyed dead bolt, keyless bolting device, sliding door pin lock, or sliding door security bar installed before September 1, 1993, may be installed not more than 54 inches from the floor.

(f) [(h)]  A keyed dead bolt or keyless dead bolt, as described by Section 757.001(6)(A)(i), installed in a dwelling on or after September 1, 1993, must have a bolt with a throw of not less than one inch.

SECTION 7.  Section 757.007, Health and Safety Code, is amended to read as follows:

Sec. 757.007.  WINDOW AND WINDOW SCREENS.  A wall of a building constructed after [before] January 1, 1994, may not be used as part of a pool yard enclosure unless each window in the wall has a latch and unless each window screen on a window in the wall is affixed by a window screen latch, screws, or similar means.  This section does not require the installation of window screens.  [A wall of a building constructed on or after January 1, 1994, may not be used as part of a pool yard enclosure unless each ground floor window in the wall is permanently closed and unable to be opened.]

SECTION 8.  Section 757.009, Health and Safety Code, is amended to read as follows:

Sec. 757.009.  INSPECTION, REPAIR, AND MAINTENANCE.  (a)  An owner of a multiunit rental complex [or a rental dwelling in a condominium, cooperative, or town home project] with a pool [or a property owners association that owns, controls, or maintains a pool] shall exercise ordinary and reasonable care to inspect, maintain, repair, and keep in good working order the pool yard enclosures, gates, and self-closing and self-latching devices required by this chapter and within the control of the owner [or property owners association].

(b)  An owner of a multiunit rental complex [or a rental dwelling in a condominium, cooperative, or town home project] with a pool [or a property owners association that owns, controls, or maintains a pool] shall exercise ordinary and reasonable care to maintain, repair, and keep in good working order the window latches, sliding door handle latches, sliding door pin locks, and sliding door security bars required by this chapter and within the control of the owner [or property owners association] after request or notice from the tenant that those devices are malfunctioning or in need of repair or replacement.  A request or notice under this subsection may be given orally unless a written lease applicable to the tenant [or written rules governing the property owners association] require the request or notice to be in writing.  The requirement in the lease [or rules] must be in capital letters and underlined or in 10-point boldfaced print.

(c)  An owner of a multiunit rental complex [or a rental dwelling in a condominium, cooperative, or town home project] with a pool [or a property owners association that owns, controls, or maintains a pool] shall inspect the pool yard enclosures, gates, and self-closing and self-latching devices on gates no less than once every 31 days.

(d)  An owner's [or property owners association's] duty of inspection, repair, and maintenance under this section may not be waived under any circumstances and may not be enlarged except by written agreement with a tenant or occupant of a multiunit rental complex [or a member of a property owners association] or as may be otherwise allowed by this chapter.

SECTION 9.  Section 757.010, Health and Safety Code, is amended to read as follows:

Sec. 757.010.  COMPLIANCE WITH CHAPTER.  (a)  Except as provided by Subsection (b) and Section 757.011, a person who constructs or modifies a pool yard enclosure to conform with this chapter may not be required to construct the enclosure differently by a local governmental entity[, common law,] or any other law.

(b)  An owner of a multiunit rental complex [or a rental dwelling in a condominium, cooperative, or town home project] with a pool [or a property owners association that owns, controls, or maintains a pool] may, at the person's option, exceed the standards of this chapter or those adopted by the Texas Board of Health under Section 757.011.  A tenant or occupant in a multiunit rental complex [and a member of a property owners association] may, by express written agreement, require the owner of the complex [or the association] to exceed those standards.

(c)  A municipality may [continue to] require greater [overall height] requirements for pool yard enclosures if the pool is owned and operated solely by the municipality [requirements exist under the municipality's ordinances on January 1, 1994].

SECTION 10.  Section 757.011, Health and Safety Code, is amended to read as follows:

Sec. 757.011.  AUTHORITY OF TEXAS BOARD OF HEALTH; VARIANCES.  (a)  In extenuating circumstances, the [The] Texas Board of Health may adopt rules requiring standards for design and construction of pool yard enclosures that exceed the requirements of this chapter and that apply to all pools and pool yards subject to this chapter.  An owner of a multiunit rental complex [or a rental dwelling in a condominium, cooperative, or town home project] with a pool [or a property owners association that owns, controls, or maintains a pool] shall comply with and shall be liable for failure to comply with those rules to the same extent as if they were part of this chapter.

(b)  The Texas Department of Health may grant a variance to the requirements of this chapter in unusual or extenuating circumstances if the variance does not allow the pool to be an attractive nuisance.

SECTION 11.  Section 757.012, Health and Safety Code, is amended to read as follows:

Sec. 757.012.  ENFORCEMENT.  (a)  A tenant of an owner of a multiunit rental complex, [a member of a property owners association,] a governmental entity, or any other person or the person's representative may maintain an action against the owner [or property owners association] for failure to comply with the requirements of this chapter.   In that action, the person may obtain:

(1)  a court order directing the owner [or property owners association] to comply with this chapter;

(2)  a judgment against the owner [or property owners association] for actual damages resulting from the failure to comply with the requirements of this chapter;

(3)  a judgment against the owner [or property owners association] for punitive damages resulting from the failure to comply with the requirements of this chapter if the actual damages to the person were caused by the owner's [or property owners association's] intentional, malicious, or grossly negligent actions;

(4)  a judgment against the owner [or property owners association] for actual damages, and if appropriate, punitive damages, where the owner [or association] was in compliance with this chapter at the time of the pool-related damaging event but was consciously indifferent to access being repeatedly gained to the pool yard by unauthorized persons; or

(5)  a judgment against the owner [or property owners association] for a civil penalty of not more than $5,000 if the owner [or property owners association] fails to comply with this chapter within a reasonable time after written notice by a tenant of the multiunit rental complex [or a member of the property owners association].

(b)  A court may award reasonable attorney fees and costs to the prevailing party in an action brought under Subsection (a)(5).

(c)  The attorney general, a local health department, a municipality, or a county having jurisdiction may enforce this chapter by any lawful means, including inspections, permits, fees, civil fines, criminal prosecutions, and injunctions[, and, after required notice, governmental construction or repair of pool yard enclosures that do not exist or that do not comply with this chapter].

SECTION 12.  Section 757.014, Health and Safety Code, is amended to read as follows:

Sec. 757.014.  APPLICATION TO OTHER BODIES OF WATER AND RELATED FACILITIES.  The owner of a multiunit rental complex [or a property owners association] is not required to enclose a body of water or construct barriers between the owner's [or property owners association's] property and a body of water such as an ocean, bay, lake, pond, bayou, river, creek, stream, spring, reservoir, stock tank, culvert, drainage ditch, detention pond, or other flood or drainage facility.

SECTION 13.  Section 757.015, Health and Safety Code, is amended to read as follows:

Sec. 757.015.  EFFECT ON OTHER LAWS.  (a)  The duties established by this chapter for an owner of a multiunit dwelling project coincide with[, an owner of a dwelling in a condominium, cooperative, or town home project, and a property owners association supersede] those established by common law, and supersede those established by the Property Code, the Health and Safety Code, the Local Government Code [other than Section 214.101], and local ordinances relating to duties to inspect, install, repair, or maintain:

(1)  pool yard enclosures;

(2)  pool yard enclosure gates and gate latches, including self-closing and self-latching devices;

(3)  keyed dead bolts, keyless bolting devices, sliding door handle latches, sliding door security bars, self-latching and self-closing devices, and sliding door pin locks on doors that open into a pool yard area and that are owned and controlled by the owner [or property owners association]; and

(4)  latches on windows that open into a pool yard area and that are owned and controlled by the owner [or property owners association].

(b)  This chapter does not affect any duties of a rental dwelling owner, lessor, sublessor, management company, or managing agent under Subchapter D, Chapter 92, Property Code.

SECTION 14.  Section 757.001(11), Health and Safety Code, and Section 214.101, Local Government Code, are repealed.

SECTION 15.  The importance of this legislation and the crowded condition of the calendars in both houses create an emergency and an imperative public necessity that the constitutional rule requiring bills to be read on three several days in each house be suspended, and this rule is hereby suspended, and that this Act take effect and be in force from and after its passage, and it is so enacted.