By JanekH.B. No. 1915

A BILL TO BE ENTITLED

AN ACT

relating to the regulation of lawn crypts.

BE IT ENACTED BY THE LEGISLATURE OF THE STATE OF TEXAS:

SECTION 1.  Section 711.001(19), Health and Safety Code, is amended to read as follows:

(19)  "Lawn crypt" means a subsurface [concrete and reinforced steel] receptacle installed in multiple units for burial of human remains.

SECTION 2.  Chapter 711, Health and Safety Code, is amended by adding Subchapter E to read as follows:

SUBCHAPTER E.  LAWN CRYPTS

Sec. 711.061.  REQUIREMENTS FOR LAWN CRYPTS. A lawn crypt may not be installed unless:

(1)  the lawn crypt is constructed of concrete and reinforced steel or other comparably durable material;

(2)  the lawn crypt is installed on not less than six inches of rock, gravel, or other drainage material;

(3)  the lawn crypt contains a method to drain water out of the lawn crypt;

(4)  the outside top surface of the lawn crypt at the time of installation is not less than 1-1/2 feet below the surface of the ground as required by Section 714.001(a)(2) and is capable of withstanding the weight of the soil and sod above the top surface and the weight of machinery and equipment normally used in the maintenance of the cemetery;

(5)  the lawn crypt is installed in a garden or other section of the cemetery that has been dedicated for lawn crypt interment purposes in accordance with Section 711.034; and

(6)  except as provided by Section 711.062, the lawn crypt is installed in multiple units of 10 or more.

Sec. 711.062.  REQUEST TO INSTALL LAWN CRYPT IN FEWER THAN 10 UNITS. A lawn crypt may be installed in fewer than 10 units if it is installed in a plot pursuant to the plot owner's written request that is in substantially the following form:

"REQUEST FOR INSTALLATION OF A LAWN CRYPT IN

FEWER THAN 10 UNITS

I, (plot owner's name and address), request (name of cemetery organization) to install a lawn crypt consisting of (number of) units in the following location (description of plots) in (name and address of cemetery).

The lawn crypt must meet the requirements of Section 711.061, Health and Safety Code:

(1)  the lawn crypt must be constructed of concrete and reinforced steel or other comparably durable material;

(2)  the lawn crypt must be installed on not less than six inches of rock, gravel, or other drainage material;

(3)  the lawn crypt must contain a method to drain water out of the lawn crypt;

(4)  the outside top surface of the lawn crypt at the time of installation must not be less than 1-1/2 feet below the surface of the ground as required by Section 714.001(a)(2), Health and Safety Code, and be capable of withstanding the weight of the soil and sod above the top surface and the weight of machinery and equipment normally used in the maintenance of the cemetery; and

(5)  the plot in which the lawn crypt is to be installed must be located in a garden or other section of the cemetery that is dedicated for lawn crypt interment purposes in accordance with Section 711.034, Health and Safety Code.

Dated (month, day, year).

(signature of plot owner)."

SECTION 3.  This Act takes effect September 1, 1997, and applies to the installation of lawn crypts on or after that date.

SECTION 4.  The importance of this legislation and the crowded condition of the calendars in both houses create an emergency and an imperative public necessity that the constitutional rule requiring bills to be read on three several days in each house be suspended, and this rule is hereby suspended.