By:  Bonnen (Senate Sponsor - Jackson)H.B. No. 2296

(In the Senate - Received from the House April 28, 1999; April 29, 1999, read first time and referred to Committee on Economic Development; May 6, 1999, reported favorably by the following vote:  Yeas 6, Nays 0; May 6, 1999, sent to printer.)

A BILL TO BE ENTITLED

AN ACT

relating to the regulation of boilers.

BE IT ENACTED BY THE LEGISLATURE OF THE STATE OF TEXAS:

SECTION 1.  Section 755.001, Health and Safety Code, is amended to read as follows:

Sec. 755.001.  DEFINITIONS. In this chapter:

(1)  "Alteration" means a substantial change in an original design.

(2)  "Board" means the board of boiler rules.

(3)  "Boiler" means:

(A)  a heating boiler;

(B)  a nuclear boiler;

(C)  a power boiler; [or]

(D)  an unfired steam boiler; or

(E)  a process steam generator.

(4)  "Certificate inspection" means the required internal or external [a] boiler inspection, the report of which is used by the chief inspector to decide whether to issue a certificate of operation.

(5)  "Certificate of operation" means a certificate issued by the commissioner to allow the operation of a boiler.

(6)  "Commissioner" means the commissioner of licensing and regulation.

(7)  "Department" means the Texas Department of Licensing and Regulation.

(8)  "External inspection" means an inspection of the exterior of a boiler and its appurtenances that is made, if possible, while the boiler is in operation.

(9)  "Heating boiler" means a steam heating boiler, hot water heating boiler, hot water supply boiler, or [lined] potable water heater that is directly fired with oil, gas, solar energy, electricity, coal, or other solid or liquid fuel.

(10)  "High-temperature water boiler" means a water boiler designed for operation at pressures exceeding 160 pounds per square inch or temperatures exceeding 250 degrees Fahrenheit.

(11)  "Hot water heating boiler" means a boiler designed for operation at a pressure not exceeding 160 pounds per square inch or temperatures not exceeding 250 degrees Fahrenheit at or near the boiler outlet.

(12)  "Hot water supply boiler" means a boiler designed for operation at pressures not exceeding 160 pounds per square inch or temperatures not exceeding 250 degrees Fahrenheit at or near the boiler outlet if the boiler's:

(A)  heat input exceeds 200,000 British thermal units per hour;

(B)  water temperature exceeds 210 degrees Fahrenheit; or

(C)  nominal water-containing capacity exceeds 120 gallons.

(13)  "Inspection agency" means an authorized inspection agency providing inspection services.

(14)  "Inspector" means the chief inspector, a deputy inspector, or an authorized inspector.

(15)  "Internal inspection" means a complete and thorough inspection of the interior waterside and fireside areas of a boiler as construction allows.

(16)  "Nuclear boiler" means a nuclear power plant system, including its pressure vessels, piping systems, pumps, valves, and storage tanks, that produces and controls an output of thermal energy from nuclear fuel and the associated systems essential to the function of the power system.

(17)  "Portable power boiler" means a boiler primarily intended for use at a temporary location.

(18)  "Potable water heater" means a boiler designed for operation at pressures not exceeding 160 pounds per square inch and water temperatures not exceeding 210 degrees Fahrenheit if the boiler's:

(A)  heat input exceeds 200,000 British thermal units per hour; or

(B)  nominal water-containing capacity  exceeds 120 gallons.

(19)  "Power boiler" means:

(A)  a high-temperature water boiler; or

(B)  a boiler in which steam is generated at a pressure exceeding 15 pounds per square inch for a purpose external to the boiler.

(20)  "Process steam generator" means an evaporator, heat exchanger, or vessel in which steam is generated by the use of heat resulting from the operation of a processing system that contains a number of pressure vessels, such as used in the manufacture of chemical and petroleum products.

(21) [(19)]  "Repair" means the work necessary to return a boiler to a safe and satisfactory operating condition without changing the original design.

(22)  "Safety appliance" means a safety device such as a safety valve or a safety relief valve for a boiler provided to diminish the danger of accidents.

(23)  "Standard boiler" means a boiler that bears a Texas stamp, the stamp of a nationally recognized engineering professional society, or the stamp of any jurisdiction that has adopted a standard of construction equivalent to the standard required by the commissioner.

(24) [(20)]  "Steam heating boiler" means a boiler designed for operation at pressures not exceeding 15 pounds per square inch.

(25) [(21)]  "Unfired steam boiler" means an unfired pressure vessel in which steam is generated.  The term does not include [a steam generating system that includes]:

(A)  vessels known as evaporators or [;

[(B)]  heat exchangers; or

(B) [(C)]  vessels in which steam is generated by using the heat that results from the operation of a processing system that contains a number of pressure vessels, as used in the manufacture of chemical and petroleum products.

SECTION 2.  Section 755.022(a), Health and Safety Code, is amended to read as follows:

(a)  This chapter does not apply to:

(1)  boilers owned or operated by the federal government;

(2)  pressure vessels or process steam generators [unfired steam boilers], other than steam collection or liberation drums of process steam generators [unfired steam boilers]; [or]

(3)  manually fired miniature boilers that:

(A)  are constructed or maintained for locomotives, boats, tractors, or stationary engines only as a hobby for exhibition, recreation, education, or historical purposes and not for commercial use;

(B)  have an inside diameter of 12 inches or less or a grate area of two square feet or less; and

(C)  are equipped with a safety valve of adequate size, a water level indicator, and a pressure gauge; or

(4)  boilers that are designed for operation only at atmospheric pressure and that are equipped with two independent means to prevent the buildup of pressure.

SECTION 3.  Sections 755.025(a) and (b), Health and Safety Code, are amended to read as follows:

(a)  The commissioner shall require each boiler to be inspected internally and externally at the time of initial installation and at subsequent intervals as provided by this section.  The commissioner may provide that the inspection be performed by any inspector.

(b)  Power boilers, unfired steam boilers, and steam collection  or liberation drums of process steam generators must receive an annual certificate inspection and an annual external inspection.

SECTION 4.  Section 755.026(a), Health and Safety Code, is amended to read as follows:

(a)  With the approval of the commissioner and the inspection agency that has jurisdiction for the power boiler, the interval between internal inspections may be extended to a period not exceeding a total of 48 months. For other unfired steam boilers or steam collection or liberation drums of process steam generators, the inspection interval may be extended to the next scheduled downtime of the boiler, but not exceeding a total of 84 months.

SECTION 5.  Section 755.027(a), Health and Safety Code, is amended to read as follows:

(a)  Not later than the 30th day after the date on which a certificate inspection is performed by an authorized inspector, the inspection agency employing the authorized inspector shall file a report with the commissioner in the manner specified by the department [stating:

[(1)  the condition of the boiler;

[(2)  the location of the boiler;

[(3)  the date of the inspection; and

[(4)  the name of the inspector].

SECTION 6.  Section 755.029(a), Health and Safety Code, is amended to read as follows:

(a)  The commissioner shall issue to the owner or operator of a boiler a certificate of operation for the boiler if [it is found] after a certificate inspection:

(1)  the boiler is found to be in a safe condition for operation; and

(2)  the owner or operator has paid the fees assessed under Section 755.030.

SECTION 7.  Sections 755.032(b), (c), and (d), Health and Safety Code, are amended to read as follows:

(b)  [The commissioner may adopt rules establishing inspection procedures for the use of nondestructive examination equipment to comply with the inspection requirements under Section 755.025.

[(c)]  The commissioner may exchange information, including data on experience, with other authorities that inspect boilers or their appurtenances, to obtain information necessary to adopt rules.

(c) [(d)]  The commissioner or a department employee may not prescribe the make, brand, or kind of boilers or any appurtenances on the boiler to purchase.

SECTION 8.  This Act takes effect September 1, 1999.

SECTION 9.  The importance of this legislation and the crowded condition of the calendars in both houses create an emergency and an imperative public necessity that the constitutional rule requiring bills to be read on three several days in each house be suspended, and this rule is hereby suspended.

* * * * *