By LucioS.B. No. 623

A BILL TO BE ENTITLED

AN ACT

relating to certain requirements applicable to the construction of speculative homes.

BE IT ENACTED BY THE LEGISLATURE OF THE STATE OF TEXAS:

SECTION 1.  Subchapter X, Chapter 2306, Government Code, is amended by adding Section 2306.514 to read as follows:

Sec. 2306.514.  SPECULATIVE HOMES. (a)  In this section, "speculative home" means a single-family dwelling that is:

(1)  constructed for sale on the open market; and

(2)  not constructed for immediate occupancy.

(b)  If a speculative home is subsidized with state or federal money administered by the department, the home must be constructed so that:

(1)  at least one entrance door, whether located at the front, side, or back of the building:

(A)  is on an accessible route served by a ramp or no-step entrance; and

(B)  has a net clear opening of at least 32 inches;

(2)  on the first floor of the building:

(A)  each interior door has a net clear opening of at least 32 inches, unless the door provides access only to a closet of fewer than 15 square feet in area;

(B)  each hallway has a width of at least 36 inches and is level, with ramped or beveled changes at each door threshold;

(C)  each bathroom wall is reinforced for potential installation of grab bars;

(D)  each electrical panel or breaker box, light switch, or thermostat is not higher than 48 inches above the floor; and

(E)  each electrical plug or other receptacle is at least 15 inches above the floor; and

(3)  each breaker box is located inside the building on the first floor.

(c)  A person who builds a home to which this section applies may obtain a waiver of the requirement described by Subsection (b)(1)(A) if the cost of grading the terrain to meet the requirement is prohibitively expensive.  A person must request the waiver from the appropriate governmental authority authorized to issue building permits or otherwise regulate the construction of buildings in the area in which the speculative home is located.

SECTION 2.  The change in law made by this Act applies only to a speculative home for which new construction begins on or after the effective date of this Act.  A speculative home for which new construction begins before the effective date of this Act is covered by the law in effect when the construction began, and the former law is continued in effect for that purpose.

SECTION 3.  This Act takes effect September 1, 1999.

SECTION 4.  The importance of this legislation and the crowded condition of the calendars in both houses create an emergency and an imperative public necessity that the constitutional rule requiring bills to be read on three several days in each house be suspended, and this rule is hereby suspended.