By:  Armbrister	S.B. No. 781

(In the Senate - Filed February 28, 2003; March 5, 2003, read first time and referred to Committee on Natural Resources; April 29, 2003, reported adversely, with favorable Committee Substitute by the following vote:  Yeas 9, Nays 0; April 29, 2003, sent to printer.)

COMMITTEE SUBSTITUTE FOR S.B. No. 781		By:  Barrientos

A BILL TO BE ENTITLED

AN ACT

relating to performance standards for toilets and water leak detection systems.

BE IT ENACTED BY THE LEGISLATURE OF THE STATE OF TEXAS:

SECTION 1.  Section 372.002, Health and Safety Code, is amended by adding Subsections (b-1), (b-2), and (b-3) and amending Subsection (c) to read as follows:

(b-1)  In addition to the requirements of Subsection (b), for a gravity flush toilet, the maximum flow may not exceed 2.0 gallons of water per flushing if a non-early-closure flapper is installed or if the water level in the tank is raised to the maximum allowable height of the overflow tube.

(b-2)  The water saving performance standards for a water leak detection system are the more restrictive of:

(1)  the standards established by the Uniform Plumbing Code and the International Association of Plumbing and Mechanical Officials and in effect on September 1, 2003; or

(2)  the following standards:

(A)  the system must sound a continuous alarm and shut off a valve on the main water line coming into the structure immediately on detecting a water leak;

(B)  the system must be listed by Underwriters Laboratories; and

(C)  the system must have a means to reset the system so as to restore water flow once the water leak has been located.

(b-3)  All new home construction and all home construction involving substantial remodeling shall include a water leak detection system that meets the water saving performance standards in Subsection (b-2).

(c)  The commission shall make and maintain a current list of plumbing fixtures and water leak detection systems that are certified to the commission by the manufacturer or importer to meet the water saving performance standards established by Subsections [Subsection] (b), (b-1), and (b-2).  To have a plumbing fixture or water leak detection system included on the list, a manufacturer or importer must supply to the commission, in the form prescribed by the commission, the identification and the performance specifications of the plumbing fixture or water leak detection system.  The manufacturer or importer must submit test results from an independent laboratory to verify that a toilet described by Subsection (b-1) meets the standards of that subsection. The commission may test a listed fixture or water leak detection system to determine the accuracy of the manufacturer's or importer's certification and shall remove from the list a fixture or system the commission finds to be inaccurately certified.

SECTION 2.  (a)  This Act takes effect September 1, 2003.

(b)  The change in law made by Subsection (b-1), Section 372.002, Health and Safety Code, as added by this Act, applies only to a toilet described by that subsection that is sold, offered for sale, distributed, or imported into this state for use in this state on or after September 1, 2005.

(c)  The change in law made by Subsection (b-3), Section 372.002, Health and Safety Code, as added by this Act, applies only to new home construction and home construction involving substantial remodeling that begins on or after January 1, 2004.

* * * * *