81R6852 SMH-F

By:  Hancock	H.B. No. 2255

A BILL TO BE ENTITLED

AN ACT

relating to restrictions on the release into the air of natural gas and associated vapors from a gas well.

BE IT ENACTED BY THE LEGISLATURE OF THE STATE OF TEXAS:

SECTION 1.  Section 86.185, Natural Resources Code, is amended to read as follows:

Sec. 86.185.  RESTRICTIONS ON RELEASE OF [PROHIBITION AGAINST] GAS IN AIR:  GAS WELLS IN GENERAL.  (a)  This section does not apply to a gas well to which Section 86.186 applies.

(b)  No gas from a gas well may be permitted to escape into the air after the expiration of 10 days from the time the gas is encountered in the gas well, or from the time of perforating the casing opposite a gas-bearing zone if casing is set through the zone, whichever is later, but the commission may permit the escape of gas into the air for an additional time if the operator of a well or other facility presents information to show the necessity for the escape;  provided that the amount of gas which is flared under that authority is charged to the operator's allowable production.  A necessity includes but is not limited to the following situations:

(1)  cleaning a well of sand or acid or both following stimulation treatment of a well; and

(2)  repairing or modifying a gas-gathering system.

SECTION 2.  Subchapter F, Chapter 86, Natural Resources Code, is amended by adding Section 86.186 to read as follows:

Sec. 86.186.  RESTRICTIONS ON RELEASE OF GAS IN AIR:  GAS WELLS IN THE NEWARK, EAST (BARNETT SHALE) FIELD.  (a)  This section applies only to a gas well that is anticipated to be or has been completed or recompleted in the Newark, East (Barnett Shale) Field.

(b)  Gas from a gas well may not be permitted to escape into the air after the second day after the date gas is encountered in the well, except that the commission may permit the escape of gas into the air for an additional period if the operator of the well or other facility presents information to show the necessity for the escape.  The amount of gas flared under the commission's authority shall be charged to the operator's allowable production.  A necessity includes the following situations:

(1)  to avoid endangering the safety of persons performing work on the well or of the public;

(2)  to drill the initial exploratory well in a field before a sales pipeline to which gas produced from the field may be delivered has been constructed;

(3)  to comply with an oil or gas lease entered into  before September 1, 2009; and

(4)  to repair or modify a gas-gathering system.

(c)  An operator of a gas well shall use techniques or methods that minimize the release into the air of gas and associated vapors when gas from the well is permitted to flow during the completion or recompletion of the well.  After a gas well is fractured or refractured, the operator as soon as practicable shall employ appropriate equipment and processes to minimize the release into the air of gas and associated vapors and:

(1)  take necessary actions to deliver salable gas to the sales pipeline; or

(2)  shut the well in and conserve the gas.

SECTION 3.  Section 86.012(a), Natural Resources Code, is amended to read as follows:

(a)  The term "waste" includes:

(1)  the operation of an oil well or wells with an inefficient gas-oil ratio;

(2)  the drowning with water of a stratum or part of a stratum capable of producing gas in paying quantities;

(3)  permitting a gas well to burn wastefully;

(4)  the creation of unnecessary fire hazards;

(5)  physical waste or loss incident to or resulting from so drilling, equipping, or operating a well or wells as to reduce or tend to reduce the ultimate recovery of gas from any pool;

(6)  the escape of gas from a well producing both oil and gas into the open air in excess of the amount that is necessary in the efficient drilling or operation of the well;

(7)  the production of gas in excess of transportation or market facilities or reasonable market demand for the type of gas produced;

(8)  the use of gas for the manufacture of carbon black without first having extracted the natural gasoline content from the gas, except it shall not be necessary to first extract the natural gasoline content from the gas where it is utilized in a plant producing an average recovery of not less than five pounds of carbon black to each 1,000 cubic feet of gas;

(9)  the use of sweet gas produced from a gas well for the manufacture of carbon black unless it is used in a plant producing an average recovery of not less than five pounds of carbon black to each 1,000 cubic feet and unless the sweet gas is produced from a well located in a common reservoir producing both sweet and sour gas;

(10)  permitting gas produced from a gas well to escape into the air before or after the gas has been processed for its gasoline content, unless authorized as provided in Section 86.185 or 86.186 [of this code];

(11)  the production of natural gas from a well producing oil from a stratum other than that in which the oil is found unless the gas is produced in a separate string of casing from that in which the oil is produced;

(12)  the production of more than 100,000 cubic feet of gas to each barrel of crude petroleum oil unless the gas is put to one or more of the uses authorized for the type of gas so produced under allocations made by the commission or unless authorized as provided in Section 86.185 or 86.186 [of this code]; and

(13)  underground waste or loss however caused and whether or not defined in other subdivisions of this section.

SECTION 4.  This Act takes effect immediately if it receives a vote of two-thirds of all the members elected to each house, as provided by Section 39, Article III, Texas Constitution.  If this Act does not receive the vote necessary for immediate effect, this Act takes effect September 1, 2009.