83R21261 SCL-F

By:  Lucio III, Larson, Isaac, Canales	H.B. No. 1973

A BILL TO BE ENTITLED

AN ACT

relating to the provision of water by a public utility or water supply or sewer service corporation for use in fire suppression.

BE IT ENACTED BY THE LEGISLATURE OF THE STATE OF TEXAS:

SECTION 1.  Subchapter C, Chapter 341, Health and Safety Code, is amended by adding Section 341.0359 to read as follows:

Sec. 341.0359.  FIRE HYDRANT FLOW STANDARDS.  (a)  In this section:

(1)  "Municipal utility" means a retail public utility, as defined by Section 13.002, Water Code, that is owned by a municipality.

(2)  "Residential area" means an area used principally for private residences that is improved with at least 100 single-family homes and has an average density of one home per half acre.

(3)  "Utility" includes a "public utility" and "water supply or sewer service corporation" as defined by Section 13.002, Water Code.

(b)  The governing body of a municipality by ordinance may adopt standards set by the commission under Subsection (c) requiring a utility to maintain a minimum sufficient water flow and pressure to fire hydrants in a residential area located in the municipality or the municipality's extraterritorial jurisdiction.

(c)  The commission by rule shall establish standards for adoption by a municipality under Subsection (b).  The standards:

(1)  in addition to a utility's maximum daily demand, must provide, for purposes of emergency fire suppression, for:

(A)  a minimum sufficient water flow of at least 250 gallons per minute for at least two hours; and

(B)  a minimum sufficient water pressure of at least 20 pounds per square inch;

(2)  must require a utility to maintain at least the minimum sufficient water flow and pressure described by Subdivision (1) in fire hydrants in a residential area located within the municipality or the municipality's extraterritorial jurisdiction;

(3)  must be based on the density of connections, service demands, and other relevant factors;

(4)  notwithstanding Subdivisions (1) and (2), if the municipality owns a municipal utility, may not require another utility located in the municipality or the municipality's extraterritorial jurisdiction to provide water flow and pressure in a fire hydrant greater than that provided by the municipal utility as determined by the commission; and

(5)  if the municipality does not own a municipal utility, may not require a utility located in the municipality or the municipality's extraterritorial jurisdiction to provide a minimum sufficient water flow and pressure greater than the standard established under Subdivision (1).

(d)  An ordinance under Subsection (b) may not require a utility to build, retrofit, or improve infrastructure in existence at the time the ordinance is adopted.

(e)  A municipality that adopts standards under Subsection (b) or that seeks to use a utility's water for fire suppression shall enter into a written memorandum of understanding with the utility to provide for:

(1)  the necessary testing of fire hydrants; and

(2)  other relevant issues pertaining to the use of the water and maintenance of the fire hydrants to ensure compliance with this section.

(f)  A municipality may notify the commission of a utility's failure to comply with a standard adopted under Subsection (b).

(g)  On receiving the notice described by Subsection (f), the commission shall require a utility in violation of a standard adopted under this section to comply within a reasonable time established by the commission.  The commission may approve infrastructure improvements and make corresponding changes to the tariff or rate schedule of a utility that is a public utility as needed to permit compliance with this section.

(h)  Notwithstanding any provision of Chapter 101, Civil Practice and Remedies Code, to the contrary, a utility is not liable for a hydrant's or metal flush valve's inability to provide adequate water supply in a fire emergency.  This subsection does not waive a municipality's immunity under Subchapter I, Chapter 271, Local Government Code, or any other law and does not create any liability on the part of a municipality under a joint enterprise theory of liability.

SECTION 2.  This Act takes effect September 1, 2013.